## Slide 1
1. Covert the following numbers to the indicated radix numbers.
(1111011.01)2= (173.2)8= ( 123.25 )10 = ( 1111011.00100101)BCD
(10010100.0101 0010 0100)BCD= (94.524)10= (1011110.10000110001001001101110100101111000110101001111111)2= (5E.8624DD2F1A9FC)16
2. The Boolean expression A +0 is equal to (a)
(a) A (b) A’ (c) 0 (d) 1
3. The output of an OR gate with inputs A, B, and C is a 1 (HIGH) when ( d )
(a) A = 1, B = 1, C = 1 (b) A = 0, B = 0, C = 1
(c) A = 0, B = 0, C = 0 (d) only answers (a) and (b)
4. Calculate the following
(1) (00111000) BCD + (10000011) BCD= 121
(2) (00111000) 2 + (10000011) 2= 187

## Slide 2
5. Complete the following table of equivalent values. Use binary numbers with a sign bit and 7 bits for the value
Decimal | Sign-magnitude | 1’s complement code | 2’s complement code
102 | 0110 0110 | 0110 0110 | 0110 0110
-68 | 1100 0100 | 1011 1011 | 1011 1100

## Slide 3
6. Write the logic expression of a 1-bit comparator, draw the circuit, and complete the time diagram.
Logic expression:

## Slide 4
1.(10p) Write the logic expression of a 1-bit comparator, draw the circuit, and complete the time diagram.
LA>B
LA<B
LA=B

## Slide 5
7. Using Boolean algebra, simplify the following expression:
= =
8. Implement the function f(A,B)=AB’+CD by using NAND gate only.
f(A,B)=AB’+CD==NOT(NOT(A*NOT(B))*NOT(C*D))
A
B’
C
D
Y

## Slide 6
9. Simplify the following boolean functions
(1)Convert the above expression to standard SOP forms
(2) Use a Karnaugh map to reducete SOP expression
(3) Draw out the logic diagram
0 | 1 | 1 | 1
0 | 1 | 1 | 1
1 | 1 | 1 | 1
0 | 0 | 0 | 1
AB
CD
00
01
11
10
00
01
11
10

## Slide 7
10. Use a Karnaugh map to reduce the expression:
F(A,B,C,D) = m(0,4,5,7,10,13) + d(2,8,9,11,14,15)
11. Optimize the functions ƒ(a,b,c,d ) = Σm(1,3,7,11,15) + Σd(0,2,5,8) in a minimum sum-of-products expression using a Karnaugh map.

## Slide 8
The inputs to a full adder are A=1, B=0, Cin=1, The outputs are Σ=_____, Cout=________
2. if a octal-to-binary priority encoder has its 0,2,5,and 6 inputs at the active level, the active-HIGH binary output is ()
(a) 110 (b) 010 (c) 101 (d) 000
0
1
A

## Slide 9
4. Give the truth table of a 1-bit full adder, and implement it using 1-of-8 multiplexer.
a | b | ci-1 | s | ci
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
s
D0
D1
D2
D3
D4
D5
D6
D7
74LS151
G A2 A1 A0
Y
D0
D1
D2
D3
D4
D5
D6
D7
a b ci-1
0
1
1
0
1
0
0
1
ci
D0
D1
D2
D3
D4
D5
D6
D7
74LS151
G A2 A1 A0
Y
D0
D1
D2
D3
D4
D5
D6
D7
a b ci-1
0
0
0
1
0
1
1
1

## Slide 10
5. An 8-bit comparator using 74LS85 is shown. The three input of the lowest order comparator should be FA>B=_____, FA=B=______, FA<B=___.
0
1
0

## Slide 11
6. Develop a logic circuit for detecting whether a 8421BCD code is a multiple of three. If it is, the output should be true.
(a)construct the truth table;
(b) write the logic expression and simplify it;
(c) draw the logic circuit.

## Slide 12
7. Consider the three-variable function f(a,b,c) = bc’+ab’+abc
1) Give its canonical SOP and canonical POS.
2) Implement the function using nand gates only.
3) Implement the function using 3-8 decoder.
4) Implement the function using 4-16 decoder.
5) Implement the function using 1-of-4 multiplexer (use a, b as select inputs).

## Slide 13
4. Consider the 3-variable function f(a,b,c) = bc’+ab’+abc
  1) (10p) Give its canonical SOP and canonical POS.
  2) (10p) Implement the function using nand gates.
f
b
c’
1
a

## Slide 14
a
b
c
F
0
0
1
O0 O1
O2 O3 O4 O5 O6 O7
A2 A1 A0
74138
&
E1
E2 E3
4. Consider the 3-variable function f(a,b,c) = bc’+ab’+abc
  3) (15p) Implement the function using 3-line-to-8-line decoder.

## Slide 15
4. Consider the 3-variable function f(a,b,c) = bc’+ab’+abc
  4) (15p) Implement the function using 4-16 decoder.
Y0 Y1 Y2 Y3 Y4 Y5 Y6 Y7
Y8
Y9
…
Y15
A3 A2 A1 A0
Decoder
E
.
.
.
0
a
b
c
0
&
f

## Slide 16
4. Consider the 3-variable function f(a,b,c) = bc’+ab’+abc
  5) (15p) Implement the function using 1-of-4 multiplexer(use a, b as select inputs).
则，
MUX
G A1 A0
Y
D0
D1
D2
D3
f(a,b,c)
a b
0
c’
1
1

## Slide 17
8. There are 2 control signals: C1 and C2，design a circuit using a 74LS151 data selector.

## Slide 18
5. There are 2 contral signals: C1 and C2，design a circuit using an 1-of-8 MUX.
1) ， ； 2) ， ；
3) ， ； 4) ， 。
C2C1 | AB | F
0 0 0 0 0 0 0 0 | 0 0 0 1 1 0 1 1 | 0 1 1 0
0 1 0 1 0 1 0 1 | 0 0 0 1 1 0 1 1 | 1 1 1 0
1 0 1 0 1 0 1 0 | 0 0 0 1 1 0 1 1 | 1 0 0 0
1 1 1 1 1 1 1 1 | 0 0 0 1 1 0 1 1 | 0 0 0 1
C2 C1 A
D0
D1
D2
D3
D4
D5
D6
D7
MUX
74LS151
G A2 A1 A0
F
Y
D0
D1
D2
D3
D4
D5
D6
D7
B
B’
1
B’
B’
0
0
B

## Slide 19
1. A modulus-13 counter has 13 states requiring __ flip-flops. A modulus-13 ring counter requiring ____ flip-flops.
2. Assume the clock for a 3-bit binary counter is 16MHz. The output frequency of the third stage (Q2) is ( )
a. 2MHz b. 128MHz c. 5.33MHz d. 48MHz
3. An asynchronous counter differs from a synchronous counter in ( ).
a. the number of states in its sequence. b. the method of clocking.
c. the type of flip-flops used. d. the value of the modulus.
a
4
13
b
2n
n

## Slide 20
4. A 4-bit binary up/down counters is in the binary state of 0111. The next state in the DOWN mode is
5. List the true tables and the characteristic equations of SR flip-flop, JK flip-flop and D flip-flop
0110

## Slide 22
6. In the figure for this problem, complete the timing diagram for a positive edge triggered J-Kflip-flop.

## Slide 23
set reset toggle toggle

## Slide 24
7. Given the logic diagram and CP for this problem, complete the Q0, Q1 and Q2 waveforms.

## Slide 26
8. Design a counter to produce the following binary sequence with J-K flip-flops: 1, 4, 3, 5, 7, 6, 2, 1,...
001
100
011
101
111
110
010
Q1Q2Q3
101
001
011
111
100
110
010
1
0
0
1
1
1
0
0
0
1
1
0
1
1
1
1
1
1
0
0
0
Q1n+1
Q2n+1
Q3n+1
X
X
X
Q1n+1 = Q3
Q2n+1 = Q1
Q3n+1 = Q1+Q

## Slide 27
Q1n+1 = Q3(Q1+)
Q2n+1 = Q1(Q2+)
Q3n+1 = (Q1Q2)(Q3+)
Q1n+1 = Q3+Q3Q1
Q2n+1 = Q1+Q1Q2
Q3n+1 = (Q1+(Q1Q2)Q3
J1 = Q3, K1 =
J2 = Q1,K2 =
J3=(Q1,K3=
J
C
K
Q
J
C
K
Q
J
C
K
Q
ff1
ff2
ff3

## Slide 28
9. Construct a Mealy state diagram that will detect a serial input sequence of 01010

## Slide 29
10. Using counter to realize following control signals E1,E2, E3.
E1: 0010, 0011, 1000 , 1001, 1010, 1011
E2 : 0101
E3 : 1001