## Slide 1
Chapter 9 Counters

## Slide 2
Counters计数器
A counter is a register that goes through a predetermined sequence of states upon the application of clock pulses.
Counters are categorized as:
  Asynchronous Counter(Ripple Counters):The FF output transition serves as a source for triggering other FFs. No common clock.
  Synchronous Counter:All FFs receive the common clock pulse, and the change of state is determined from the present state.
Notes: 能够记忆输入脉冲个数的电路称为计数器。它在时钟脉冲的作用下，根据预定义的状态序列完成计数。
分类：
异步计数器（也称行波计数器）
  无共同时钟，触发器的输出转换作为其他触发器的触发来源。
同步计数器
  有共同时钟，所有触发器接受公共时钟脉冲，状态的改变由现态决定。

## Slide 3
6
1
CP
5
4
2
3
Q
0
1
0
1
0
1
0
Asynchronously clocked modulus-2 binary counter
(异步模2二进制计数器)

## Slide 4
6
1
CP
5
4
2
3
Q1
Q2
0
0
1
0
0
1
1
1
0
0
Asynchronously clocked modulus-4 binary counter

## Slide 5
In an asynchronous counter, the clock is applied only to the first stage. Subsequent stages derive the clock from the previous stage.
The three-bit asynchronous counter shown is typical. It uses J-K flip-flops in the toggle mode.
Three bit Asynchronous Counter(三位异步计数器)
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH
Notes: 首先，注意到触发器都是JK，且为上升沿触发模式。
当J、K都为1时，触发器处于翻转模式。
在异步计数器里，时钟只连接第一个计数器，后续的计数器使用前一个计数器的输出来触发。
也即较低有效位输出作为下一个较高有效位的时钟信号
注意：连接Q’的作用在于，当Q从1变成0时，Q’刚好处于从0变1.
在以后的触发器电路中，如果没有特别说明，Q0总会是最低一位。

## Slide 6
Three bit Asynchronous Counter
CLK
Q0
Q1
Q2
Notice that the Q0 output is triggered on the leading edge of the clock signal. The following stage is triggered from Q0. The leading edge of Q0 is equivalent to the trailing edge of Q0. The resulting sequence is that of an 3-bit binary up counter.
Notes: 思考：如果把上升沿触发的JK触发器换成下降沿触发的JK触发器，设计上需要如何改动？
答案：从连接Q’变成连接Q。

## Slide 7
Four bit Asynchronous Counter
A 4-bit Upward Counting Ripple Counter with negative edge-triggered J-K flip-flop:Counting from 0000~1111
How about 5-bit? 6-bit?
Notes: 注意：
JK输入都是逻辑1
时钟脉冲是负脉冲有效
每个Q输出作为下一级的时钟脉冲。最低级直接接入时钟脉冲
（依次类推，理论上可设计出任意N bit的异步计数器，可以计数从0到2N-1。）

## Slide 8
Propagation Delay(传输延迟)*
Asynchronous counters are sometimes called ripple counters, because the stages do not all change together. For certain applications requiring high clock rates, this is a major disadvantage.
Notice how delays are cumulative as each stage in a counter is clocked later than the previous stage.
CLK
Q0
Q1
Q2
Q0 is delayed by 1 propagation delay, Q2 by 2 delays and Q3 by 3 delays.
Notes: 异步计数器，有时候也称行波计数器。
触发不是立即传递达到，而是有一个延时。异步计数器的这种积累延迟，在许多应用中都是一个主要的缺点，因为它限制了计数器的运行速度，并且产生了译码问题。计数器中的最大积累延迟必须小于时钟波形的周期。

## Slide 9
Modulus-N Counters
The modulus of a counter is the number of unique states through which the counter will sequence.
计数器的模是计数器按顺序经过的独特状态的数目。
The maximum possible number of states (maximum modulus) of a counter is 2n, where n is the number of flip-flops in the counter.
包含n个触发器的计数器的最大可能状态是2n。

## Slide 10: How to implement a modulus-6 binary counter with a modulus-8 counter?
QC | QB | QA | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | d
0
0
0
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
1
1
F = (QBQC)’

## Slide 11
Asynchronous Decade Counter(异步十进制计数器)
This counter uses partial decoding to recycle the triggered, so clocks are derived from the Q outputs. Other count sequence to zero after the 1001 state. The flip-flops are trailing-edge truncated sequences(截断序列) can be obtained using a similar technique.
CLK
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
HIGH
C
J3
K3
Q3
CLR
Notes: 截断序列：设计计数器，使得其序列中的状态个数小于最大值2n。这种序列称为截断序列。
只要是有10个状态的都可以称为模10计数器。按照0000~1001排序的称为BCD模10计数器。
Decade:10个一组

## Slide 12
CLK
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
HIGH
C
J3
K3
Q3
WHY？
One way to truncate the sequence is to decode ten (1010) with an active-low output.
Partial Decoding(部分译码): the two unique states(Q1=1 and Q3=1) are sufficient to decode the count of ten.（Verify it with K-map)
Notes: 设计原理：在数完0到9以后，数到10的瞬间给出一个低信号到CLR端上，则所有计数器清0.
一种最容易想到的办法就是，设计一个1010（10）的译码器，采用4输入与非门。
但是，进一步考虑到序列的特殊性，从0000到1001，都不会同时在Q1和Q3上具有高电平，所以可以采用部分译码的形式，只使用一个二输入与非门即可。
用卡诺图也可以验证，其中0~9要求输出1，1010要求输出0，其余为任意项。则可推出Q3’+Q1’
类似的设计方法可以推任意模的计数器。

## Slide 13
Asynchronous Decade Counter
When Q1 and Q3 are HIGH together, the counter is cleared by a “glitch(毛刺)” on the CLR line.
CLK
Q0
Q1
Q2
Q3
CLR
Glitch
Glitch

## Slide 14
Quick design a asynchronous module-K counter:
Counting from 0 to K
2. Decide the number of flip-flops: 2n-1 < K ≤ 2n
3. Let all the flip-flops recycle back to 0 after the K-1 state.
K=2n.
K<2n. One way to make it is to decode K with logic gates and connect the output to the clear inputs of the flip-flops.
CLK
D
CLK
Q
Q
1. Choose the type of flip-flops.
Notes: 当然，设计的时候，要留意用的是JK触发器，还是D触发器。上升沿还是下降沿。
回忆：D计数器，如何实现翻转功能？
把Q’接到D上即可。

## Slide 15
The 74LS93A Asynchronous Counter
The 74LS93A has one independent toggle J-K flip-flop driven by CLK A and three toggle J-K flip-flops that form an asynchronous counter driven by CLK B.
The counter can be extended to form a 4-bit counter by connecting Q0 to the CLK B input. Two inputs are provided that clear the count.
All J and K inputs are connected internally HIGH
CLK A
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
C
J3
K3
Q3
CLK B
RO (1)
RO (2)
Notes: 负边沿触发。
所有JK都接高电平，也即采用了翻转模式。
两个时钟信号。
当RO1和RO2都为高时，则所有计数器清0.
如果把Q0和CLK B连接，则构成一个4位模16计数器。
74LS93A，可以实现所有模16以内的计数器。

## Slide 16
How to design modulus-N counter with 74LS93？{N=2..16}

## Slide 17
Synchronous Counters(同步计数器)
In a synchronous counter all flip-flops are clocked together with a common clock pulse.
Synchronous counters overcome the disadvantage of accumulated propagation delays, but generally they require more circuitry to control states changes.
A 2-bit synchronous binary counter
Notes: JK触发器
上升沿触发，且接入公共时钟信号
高级触发器的J-K输入由低级触发器决定。

## Slide 18
Timing details for the 2-bit synchronous counter
Notes: 实际绘图时，延时会被忽略。

## Slide 19
A 3-bit binary Synchronous Counters(三位同步计数器)
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q0Q1
Q0
Q1
Q2
CLK
HIGH
This 3-bit binary synchronous counter has the same count sequence as the 3-bit asynchronous counter shown previously.
Notes: 考虑变化情况，011转100，以及111转000，可知当Q0Q1同时为1时，下一步，Q2发生变化。

## Slide 20
A 4-bit Synchronous Binary Counter
Q0
Q1
Q2
Q3
The 4-bit binary counter has one more AND gate than the 3-bit counter just described. The shaded areas show where the AND gate outputs are HIGH causing the next FF to toggle.

## Slide 21
Sequential Circuits’ Design

## Slide 22
Sequential Circuit Models(时序电路模型)
电路存在反馈
存储元件：数据随时间自由变化
输出方程
O=f1(I,S)
激励方程
E=f2(I,S)
状态方程
St+1=f3(E,St)

## Slide 23
Mealy Vs Moore machines
Mealy model:Both outputs and next state depend both on primary inputs AND present state.
Moore model:Only next state depends directly on primary inputs AND present state. Outputs depend only on present state.
O=g(I,St)
O=g(St)
Notes: Mealy模型
  输出以及次态由输入和现态决定
Moore模型
  次态由输入和现态决定，而输出只取决于现态。

## Slide 24
State Machine Notation(状态机符号)
Imput variable
Output variable
State variable
Excitation variable
State
State variables and states are related by the expression:
2x=y
State variables
states
Notes: 输入变量(Input variable)
  源于时序机外部的所有变量
输出变量(Output variable)
  离开时序机的所有变量
状态变量(State variable)
  触发器输出
激励变量(Excitation variable）
  触发器输入
状态(State)
  由存储元件的内容来定义
状态变量与状态个数的关系： 2x=y
x：状态变量的个数
y：状态个数

## Slide 25
State Diagram (状态图)
Graphical representation of a state table.
Graph node with label s denotes state s
X
0
1
D=1
D=0
D=0
D=1
D触发器状态转换图
Graph edge with label X denotes transition between two states when input X is applied
S
Notes: 时序电路的图形化表示法
状态图中带标签S的圆形节点表示状态S。
两个状态间的，带标签的有向边表示，当标签所示条件发生时，两个状态间的转移情况。

## Slide 26: State Diagram of Mealy model
1/0
00
0/0
01
1/0
0/1
11
0/1
10
1/0
0/1
1/0
I/O
S1
S2
当现态为S1，输入I，则机器将转换到状态S2，输出O。

## Slide 27: State Diagram of Moore model
I
S1/O1
S2/O2
Reads as: When at state s1 with output
O1 and apply input I, we proceed to state s2 with Output O2.
0/0
00,11
1/1
01,10
01,10
00,11
Notes: 当现态为S1，输出为O1，输入I，则转换到S2状态，并输出O2。

## Slide 28: State Diagram
Notes: J-K触发器的两种Moore电路表示法
(a)输出变量写在状态变量名的下面
(b)用弧线表示的输出变量

## Slide 29: State Table（状态表）
Enumerates the relationship between inputs, outputs, and states of the sequential circuit.
State Table
Notes: 状态图的表状形式。列出了时序电路的输入、输出以及状态之间的关系。
右上角图中，只指出了z为真的情况

## Slide 30: State Table
State Table
Notes: 状态和触发器之间如何关联起来？通过状态转换表
先使用状态表的好处？设计完状态流程以前，并不能确定需要几个触发器。

## Slide 31: Transition Table(状态转换表)
Each state is assigned a unique code.
FA | FB | State
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D
Notes: 将特定的状态变量值分配给每一状态。
此处四个状态，22=4，需要2个触发器。

## Slide 32: Transition Table
Transition Table for state machine M1
Transition Table for state machine M1

## Slide 33: Excitation Table and Equations (激励表与激励函数)
Choose the type of flip-flops to design the state machine.
  D
  JK
  SR

## Slide 34
D flip-flop used to realize circuit (two D flip-flops)
Transition Table for state machine M1
state machine M1 excitation table using D flip-flops

## Slide 35
D flip-flop used to realize circuit (two D flip-flops)
Transition Table for state machine M1
state machine M1 excitation table using D flip-flops
How to get the equations？
DA
DB
Z

## Slide 36
DA K-Map
DA=f(FA,FB,x,y)=Σ(5,7,10,13,15)
=FAFB’xy’+FAx’y+FBy

## Slide 37
DB K-Map
DB =f(FA,FB,x,y)
=Σ(2,3,4,5,6,7,14,15)
=FA’FB+FA’x+FBx

## Slide 38
Z= f(FA,FB,x,y)=Σ(11)
=FAFB’xy
DA=FAFB’xy’+FAx’y+FBy
DB=FA’FB+FA’x+FBx
Notes: 激励实现的代价：21条逻辑门输入线。

## Slide 39
J-K flip-flop used to realize circuit (two J-K flip-flops)
state machine M1 excitation table using J-K flip-flops
Transition Table for state machine M1

## Slide 40
JA K-Map
KA K-Map
JA =f(FA,FB,x,y)
=Σ(5,7) +Σd(8,9,10,11,12,13,14,15)
=FBy
KA=f(FA,FB,x,y)
=Σ(8,11,12,14) +Σd(0,1,2,3,4,6,7)
=FB’xy+x’y’+FBy’

## Slide 41
JB K-Map
KB K-Map
JB=f(FA,FB,x,y)
=Σ(2,3) +Σd(4,5,6,7,12,13,14,15)
=FA’x
KB=f(FA,FB,x,y)
=Σ(12,13) +Σd(0,1,2,3,8,9,10,11)
=FAx’
Z= f(FA,FB,x,y)=Σ(11)
=FAFB’xy
Notes: Z只和触发器输出状态以及输入有关，和所选择的触发器类型无关。故布尔表达式不变。

## Slide 42
S-R flip-flop used to realize circuit (two SR flip-flops)
Transition Table for state machine M1
state machine M1 excitation table using S-R flip-flops

## Slide 43
SA K-Map
RA K-Map
SA=f(FA,FB,x,y)
=Σ(5,7) +Σd(9,10,13,15)
=FBy
RA=f(FA,FB,x,y)
=Σ(8,11,12,14) +Σd(0,1,2,3,4,6)
=FB’xy+x’y’+FBy’

## Slide 44
SB K-Map
RB K-Map
SB=f(FA,FB,x,y)
=Σ(2,3) +Σd(4,5,6,7,14,15)
=FA’x
RB=f(FA,FB,x,y)
=Σ(12,13) +Σd(0,1,8,9,10,11)
=FAx’

## Slide 45: Excitation Realization Cost
JA=FBy
KA=FB’xy+x’y’+FBy’
JB=FA’x
KB=FAx’

## Slide 46: Excitation Realization Cost
SA=FBy
RA=FB’xy+x’y’+FBy’
SB=FA’x
RB=FAx’

## Slide 47: Excitation Realization Cost
DA=FAFB’xy’+FAx’y+Fby DB=FA’FB+FA’x+FBx

## Slide 48
X
Y
Z
Z= FAFB’xy
Notes: 在本例中，激励实现的代价J-K和SR相对比D和T触发器要小。

## Slide 49: Sequential Circuits’ Analysis

## Slide 50: Synchronous Sequential Circuit Analysis
1.确定系统变量：输入变量、状态变量以及输出变量；
2.确定触发器类型，写出特征方程；
3.写出激励方程；
4.写出次态方程；
5.写出输出方程；
6.构造转换表；
7.为每个状态分配相应符号，构造状态图或状态表；
8.画出时序图（波形图）；
9.功能分析。

## Slide 51: Analysis Examples
E.g.1: Analysis the following synchronous sequential circuit, suppose the present state is 00, the input sequence is 0000011111, give the timing diagram.
Notes: 1.输入x
2.输出z
3.两个JK触发器负边沿触发

## Slide 52: Analysis Examples
  1. Determine the system variables: input, state, and output.
  input=x output=Z
  state variables=y1 and y0
  2. Determine the flip-flop type. Write the characteristic equations.
  yn+1=Jyn’+k’yn
  3. write the excitation equations.
  K0=J0=1
  K1=J1=x⊕y0
Notes: 1.确定系统变量：输入变量、状态变量以及输出变量；
  输入变量：x
  输出变量：z
  状态变量：y1、y0
2.确定触发器类型，写出特征方程；
  yn+1=Jyn’+K’yn
3.写出激励方程；

## Slide 53: Analysis Examples
  4. write the next state equations.
  y1n+1=J1y1’+k’y1
  =x’y1’y0 +x’y1y0’+xy1’y0’+xy1y0
  y0n+1=J0y0’+k0’y0
  =y0’
  5. Write the output variable equations.
  Z=(xy1’)’=x’+y1
  6. Construct a transition table.
  yn+1=Jyn’+k’yn
  K0=J0=1
  K1=J1=x⊕y0
Notes: 4.写出次态方程
5.写出输出方程；
6.构造转换表

## Slide 54
  y1n+1= x’y1’y0 +x’y1y0’ +xy1’y0’+xy1y0
  y0n+1=y0’
  Z=(xy1’)’=x’+y1
Y1n+1 K-Map
Z K-Map
Y0n+1 K-Map

## Slide 55
  7. Assign symbols to the states and construct a table or state diagram.
Q1 | 00
Q2 | 01
Q3 | 10
Q4 | 11
Notes: 7. 为每个状态分配相应符号，构造状态图或状态表

## Slide 56
  8. construct a timing diagram.

## Slide 57: Analysis Examples
Eg.2: Analysis the following circuit
Notes: 4个输出Q1~Q4
4个D触发器正脉冲触发

## Slide 58
  1. Determine the system variables: input, state, and output.
  state variables: Q1,Q2,Q3, and Q4
  2. Determine the flip-flop type. Write the characteristic equations.
  Qn+1=D
  3. excitation equations.
  D4=Q3
  D3=Q2
  D2=Q1 D1=Q4’(Q3Q1’)’=Q4’Q3’+Q4’Q1

## Slide 59
  4. the next state equations.
  Q4n+1=Q3
  Q3n+1=Q2
  Q2n+1=Q1
  Q1n+1=Q4’Q3’+Q4’Q1
  Qn+1=D
  D4=Q3
  D3=Q2
  D2=Q1
  D1=Q4’(Q3Q1’)’=Q4’Q3’+Q4’Q1

## Slide 60
  5. Construct a transition table.
  Q4n+1=Q3
  Q3n+1=Q2
  Q2n+1=Q1
  Q1n+1=Q4’Q3’+Q4’Q1

## Slide 61
  6. Assign symbols to the states and construct a table or state diagram.
Notes: 为每个状态分配相应符号，构造状态图或状态表

## Slide 62
CP
Q1
Q2
Q3
Q4
S0 S1 S3 S7 S15 S14 S12 S8 S0
  7. construct a timing diagram.

## Slide 63: Exercise
Find the transition table and the state table for the Mealy sequential circuit below.
Z

## Slide 64
  1. Determine the system variables: input, state, and output.
  input: x1,x2 output: Z
  state variable: Da , Db ,Dc
  2. Determine the flip-flop type. Write the characteristic equations.
  Qn+1=D
  3. Excitation equations and output equations.
  Da=Qa⊕X2
  Db=Qb⊕X1
  Dc=X1X2Qc’Qa
  Z=X1X2Qc’Qa
Z

## Slide 65
  Da=Qa⊕X2
  Db=Qb⊕X1
  Dc=X1X2Qc’Qa
  Z=X1X2Qc’Qa
  4. write the next state equations. Qan+1=QaX2’+Qa’X2
  Qbn+1=QbX1’+Qb’X1
  Qcn+1=X1X2Qc’Qa
  5. Construct a transition table.

## Slide 66
  6. Assign symbols to the states and construct a state table

## Slide 67: Construction of State Diagrams
The most challenging part of sequential circuit synthesis is the development of a state diagram from a verbal or written problem statement.
Construction of a state diagram in sequential design is analogous to the construction of a truth table in combinational logic design.
Notes: 时序电路合成过程中，最具挑战性的部分就是从口头或书面的问题描述来形成状态图。
在时序设计中构造状态图类似于在组合逻辑设计中构造真值表。

## Slide 68: Example 1:同步可逆十进制计数器
为同步可逆十进制计数器创建状态图。计数器根据模式控制输入信号的值以二进制的形式向上或向下计数。模式控制输入M=0时，计数器向上计数；M=1时，计数器向下计数。计数器可以重复或循环计数，如果向上计数且达到终止计数值，则计数器输出y为1。如果是向下计数且达到终止计数值，则另一个输出z为1。
分析： 状态个数：10（十进制）
状态转换控制：M=0向上计数，M=1向下计数
输出：y、z

## Slide 69
Solution:
  10 states: 0..9
  1 mode control, M=0/M=1，
  output y, z
0
1
2
3
4
9
8
7
6
5
M'
M'
M'
M'
M'
M'
M'
M'
M'/y
M'
M
M
M
M
M
M/z
M
M
M
M
Notes: 分析： 状态个数：10（十进制）
状态转换控制：M=0向上计数，M=1向下计数
输出：y、z
Mealy机

## Slide 70: Example 2-1: Sequence Detector
Construct a Mealy state diagram that will detect a serial input sequence of 10110. The detection of the required bit pattern can occur in a longer data string and the correct pattern can overlap with another pattern. When the input pattern has been detected, cause an output z to be asserted high.
  For example, let the input string be
  x = 10110110110
  z = 00001001001
Notes: 构造一个可以检测出串行输入序列10110的Mealy状态图。对所规定的位模式的检测能出现在较长的数据串中。正确的模式也可以和另一种模式重叠。输入模式被检测出来后，引起输出z变为高电平。
  例如：
  对于输入串x = 10110110110
  有 z = 00001001001

## Slide 71
e.g.：input 10110110110
state BCDECDECDEC
output 00001001001
A
Starting state，waiting the first 1
0/0
1/0
B
0/0
1/0
C
0/0
“1”
“10”
1/0
“101”
D
0/0
“1011”
1/0
“10”
E
1/0
“1”
0/1
“10110”

## Slide 72: Example 2-2: Sequence Detector
Design a Mealy serial bit-pattern detector that will detect the input sequence 01010 in a longer bit string. If the pattern is detected, then cause output Q to be active-high. If an 011 bit pattern occurs within the same serial data string, cause output P to be active high. If the 011 pattern occurs, cause the state machine to initialize and start over looking for the 01010 pattern. Overlapping 01010 patterns can occur.
  If X = 00110101011101010101 then output
  Q = 00000000100000001010
  P = 00010000001000000000
Notes: 设计一个可以检测较长位串中的输入序列01010的Mealy串行位模式检测器。如果该位模式被检测到，那么就使输出Q为高有效。如果模式011出现在同样的串行数据串中，使输出P为高态有效。如果模式011出现，则使状态机初始化且重新开始等待01010模式。允许出现重叠的01010模式。
  例如：
  对于输入串x = 00110101011101010101
  有 Q= 00000000100000001010
  P = 00010000001000000000

## Slide 73
e.g.：input 00110101011
state：A-B-C-A-B-C-D-E-D-E-A
output：P：0010000001
Q：0000000100
A
1
0
“0”
“0”
B
0
1
“01”
“01”
C
1/P
“011”，resets to state A
0
“010”
D
0
“0101”
1
“01”
E
1/P
“011”，resets to state A
0/Q
“01010”

## Slide 74
Synchronous Counters

## Slide 75: J-K Flip Flop Design of a 4-bit Binary Up Counter
Notes: 用JK触发器实现
Step1:确定输入变量、输出变量；
Step2:确定触发器个数
  状态个数:16->需要触发器:4;
Step3:确定触发器类型：JK触发器；
Step4:列出转换表；
Step5:列出激励表；
Step6:写出激励方程，输出方程；
Step7:画出逻辑图。

## Slide 78
Notes: Q0的JK不用卡诺图了，非1即X，显然可以设置成全1.

## Slide 79
JQ0 = 1
KQ0 = 1
JQ1 = Q0
KQ1 = Q0
JQ2 = Q0 Q1
KQ2 = Q0 Q1
JQ3 = Q0 Q1 Q2
KQ3 = Q0 Q1 Q2

## Slide 80: J-K Flip Flop Design of a Binary Up Counter with EN and CO
EN = enable control signal, when 0 counter remains in the same state, when 1 it counts
CO = carry output signal, used to extend the counter to more stages
JQ0 = 1 · EN
KQ0 = 1 · EN
JQ1 = Q0 · EN
KQ1 = Q0 · EN
JQ2 = Q0 Q1 · EN
KQ2 = Q0 Q1 · EN
JQ3 = Q0 Q1 Q2 · EN
KQ3 = Q0 Q1 Q2 · EN
CO = Q0 Q1 Q2 Q3 · EN
Notes: 含使能信号和进位输出信号的JK同步二进制计数器
EN控制计数器开始计数
CO用于扩展计数器状态

## Slide 81: Synchronous binary counters using D flip-flops
DQ0 = Q0 EN
DQ1 = Q1 ( Q0 · EN)
DQ2 = Q2 ( Q0 Q1 · EN )
DQ3 = Q3 ( Q0 Q1 Q2 · EN )
CO = Q0 Q1 Q2 Q3 · EN
JK-based design calls for 4 AND gates
D-based design calls for 4 AND and 4 XOR gates
JK-FF equations

## Slide 82
With some additional logic, a binary counter can be converted to a BCD synchronous decade counter. After reaching the count 1001, the counter recycles to 0000.
BCD Decade Counter
Q0
Q3
Exercise: desigh a BCD Decade Counter
Notes: 此处的设计在于，从波形图分析，从0000开始到0111时，Q3需要翻转，再继续，到1001以后，Q3再次需要翻转。故直接得到两个与门相或的结果。
练习要求：采用之前学习的设计模式，自行设计一个同步BCD十进制计数器。
注意：遇到1001以后，下一状态为0000.对于1010~1111的，可以采用任意项。
可以参考J-K Flip Flop Design of a 4-bit Binary Up Counter 的状态表进行设计。 如果按照卡诺图化到最简，则K3和J3可以是不同表达式。会与图中有所区别。
J3=Q2Q1Q0，K3=Q0。

## Slide 83
Waveforms for the decade counter:
BCD Decade Counter
CLK
Q0
Q1
Q2
Q3

## Slide 84
A 4-bit Synchronous Binary Counter
The 74LS163 is a 4-bit IC synchronous counter with additional features over a basic counter. It has parallel load, a CLR input, two chip enables, and a ripple count output that signals when the count has reached the terminal count.
Data inputs
Data outputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3
Notes: CLR: 清0输入
LOAD：载数信号，在下一个时钟脉冲来临时读取数据输入状态
ENT/ENP：使能，控制计数。
RCO：异步（行波）输出
RCO和使能输入可以用于计数器扩展。

## Slide 85
Data inputs
Data outputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3
Clear Preset
Count Inhibit
12 13 14 15 0 1 2
Notes: CLR: 清0输入
LOAD：载数信号，在下一个时钟脉冲来临时读取数据输入状态
ENT/ENP：使能输入
RCO：异步（行波）输出
CLR信号有效，在时钟脉冲到来后，全部清0，LOAD信号有效，下一个时钟脉冲，读入D3到D0，使能信号有效，开始计数。

## Slide 86
Up/Down Synchronous Counters(可逆同步计数器)
An up/down counter is capable of progressing in either direction depending on a control input.
CLK
Q0
Q1
Q2
K0
J0
C
C
C
J1
J2
K1
K2
HIGH
UP/DOWN
UP
DOWN
FF0
FF1
FF2
Q0.UP
Q0.DOWN
Q0
Q1
Q2

## Slide 87
Up/Down Synchronous Counters
The 74HC191 has the same inputs and outputs but is a synchronous up/down binary counter.
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 10
74HC190
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 16
74HC191
The 74HC190 is a high speed CMOS synchronous up/down decade counter with parallel load capability. It also has a active LOW ripple clock output (RCO) and a MAX/MIN output when the terminal count is reached.

## Slide 88
Cascading is a method of achieving higher-modulus counters. For synchronous IC counters, the next counter is enabled only when the terminal count of the previous stage is reached.
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
Example
Solution
a) Each counter divides the frequency by 16. Thus the modulus is 162 = 256.
Cascaded counters(级联计数器)
What is the modulus of the cascaded DIV 16 counters?
If fin =100 kHz, what is fout?
fout
b) The output frequency is 100 kHz/256 = 391 Hz
Notes: CTEN:使能输入
计数器1每完成一次计数循环，输出一次TC信号使得计数器2开始计数一次
级联效果：10*10=100

## Slide 89
Decoding is the detection of a binary number and can be done with an AND gate.
Counter Decoding(计数器译码)
Question
What number is decoded by this gate?

## Slide 90
The decade counter shown previously incorporates partial decoding (looking at only the MSB and the LSB) to detect 1001. This was possible because this is the first occurrence of this combination in the sequence.
Partial Decoding(部分译码)
Detects 1001 by looking only at two bits

## Slide 91
The divide-by-60 counter in the text also uses partial decoding to clear the tens count when a 6 was detected.
The divide characteristic illustrated here is a good way to obtain a lower frequency using a counter. For example, the 60 Hz power line can be converted to 1 Hz.
Resetting the Count with a Decoder

## Slide 92
Show how to decode state 5 with an active LOW output.
Notice that a NAND gate was used to give the active LOW output.
Counter Decoding
Example
Solution

## Slide 93
Control Signal Generation by Decoding Counter Outputs
Using counter to realize following control signals
74LS393: Dual 4-bit Binary Counter.
双四位二进制计数器

## Slide 94
E1 = f(Q3,Q2,Q1,Q0) = m(2,3,8,9,10,11)
E2 = f(Q3,Q2,Q1,Q0) = m(5)
E3 = f(Q3,Q2,Q1,Q0) = m(9)
Control Signal Generation by Decoding Counter Outputs

## Slide 95
Control Signal Generation by Decoding Counter Outputs
E1 = f(Q3,Q2,Q1,Q0) = m(2,3,8,9,10,11)
E2 = f(Q3,Q2,Q1,Q0) = m(5)
E3 = f(Q3,Q2,Q1,Q0) = m(9)

## Slide 96
A Counter Application: Digital Clock(数字时钟)

## Slide 97: Arbitrary Sequence Counter (任意序列计数器)
Given an arbitrary sequence, design a counter that will generate this sequence.
Procedure:
  Derive state table/diagram based on give sequence
  Simplify (using K-maps, etc)
  Draw logic diagram
Notes: 对任意序列，设计一个计数器来产生这个序列。
过程
  根据序列生成状态表/状态图
  化简（如：用卡诺图）
  绘制逻辑图

## Slide 98
Use D-FFs to draw the logic diagram for sequence generator (counter) for: 0  7  6  1  0 (000  111  110  001  000)
Notes: 示例：使用D触发器来产生一个序列 0 → 7 → 6 → 1 → 0 (000 → 111 → 110 → 001 → 000) 序列结束时，输出z=1。
所示表格为激励表

## Slide 99
D3 K-Map
Z K-Map
D1 K-Map
D2 K-Map
D3=Q3’Q1’+Q3Q1
D2=Q3’Q1’+Q3Q1
D1=Q1’
Z= Q3’Q1

## Slide 100
D3=Q3’Q1’+Q3Q1
D2=Q3’Q1’+Q3Q1
D1=Q1’
Z= Q3’Q1

## Slide 101
Selected Key Terms
Asynchronous
Modulus
Synchronous
Terminal count
State machine
Cascade
Not occurring at the same time.
The number of unique states through which a counter will sequence.
Occurring at the same time.
The final state in a counter’s sequence.
A logic system exhibiting a sequence of states or values.
To connect “end-to-end” as when several counters are connected from the terminal count output of one to the enable input of the next counter.

## Slide 102
1. The counter shown below is an example of
a. an asynchronous counter
b. a BCD counter
c. a synchronous counter
d. none of the above
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH
a

## Slide 103
The Q0 output of the counter shown
a. is present before Q1 or Q2
b. changes on every clock pulse
c. has a higher frequency than Q1 or Q2
d. all of the above
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH
d

## Slide 104
3. To cause a D flip-flop to toggle, connect the
a. clock to the D input
b. Q output to the D input
c. Q output to the D input
d. clock to the preset input
Quiz
c

## Slide 105
4. The 7493A asynchronous counter diagram is shown (J’s and K’s are HIGH.) To make the count have a modulus of 16, connect
a. Q0 to RO(1) and RO(2) to
b. Q3 to RO(1) and RO(2)
c. CLK A and CLK B together
d. Q0 to CLK B
Quiz
d

## Slide 106
Quiz
FF0
FF1
FF2
5. Assume Q0 is LOW. The next clock pulse will cause
a. FF1 and FF2 to both toggle
b. FF1 and FF2 to both latch
c. FF1 to latch; FF2 to toggle
d. FF1 to toggle; FF2 to latch
LOW
b

## Slide 107
Quiz
6. A 4-bit binary counter has a terminal count of
a. 4
b. 10
c. 15
d. 16
c

## Slide 108
Quiz
7. Assume the clock for a 4-bit binary counter is 80 kHz. The output frequency of the fourth stage (Q3) is
a. 5 kHz
b. 10 kHz
c. 20 kHz
d. 320 kHz
a

## Slide 109
8. A 3-bit count sequence is shown for a counter (Q2 is the MSB). The sequence is
a. 0-1-2-3-4-5-6-7-0 (repeat)
b. 0-1-3-2-6-7-5-4-0 (repeat)
c. 0-2-4-6-1-3-5-7-0 (repeat)
d. 0-4-6-2-3-7-5-1-0 (repeat)
Quiz
Q0
Q1
Q2
b

## Slide 110
9. FF2 represents the MSB. The counts that are being decoded by the 3-input AND gates are
a. 2 and 3
b. 3 and 6
c. 2 and 5
d. 5 and 6
Quiz
b

## Slide 111
10. Assume the input frequency (fin) is 256 Hz. The output frequency (fout) will be
a. 16 Hz
b. 1 kHz
c. 65 kHz
d. none of the above
Quiz
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
fout
d

## Slide 112
Answers:
1. a
2. d
3. c
4. d
5. b
6. c
7. a
8. b
9. b
10. d
Quiz

## Slide 113: HOMEWORK
1. Design a modulu-13 binary counter.
  1) asynchronous
  2) synchronous
2. Design a synchronous counter to produce the 3-bit gray code sequences:000,001,011,010,110,111,101,100,000…