## Slide 1: Chapter 2 Number Systems, Operations, and Codes

## Slide 2
The position（位置） of each digit in a weighted number system（权重数制系统） is assigned a weight based on the base（基） or radix（基数） of the system.
The radix of decimal numbers is ten, because only ten symbols (0 through 9) are used to represent any number.
The column weights of decimal numbers are powers of ten that increase from right to left beginning with 100 =1:
…105 104 103 102 101 100.
For fractional decimal numbers, the column weights are negative powers of ten that decrease from left to right:
102 101 100. 10-1 10-2 10-3 10-4 …
Decimal Numbers（十进制数）
What is the number?

## Slide 3
Decimal Numbers
Express the number 480.52 as the sum of values of each digit.
Example
Solution
Decimal numbers can be expressed as the sum of the products of each digit times the column value for that digit.
Thus, the number 9240 can be expressed as
(9 x 103) + (2 x 102) + (4 x 101) + (0 x 100)
or
9 x 1,000 + 2 x 100 + 4 x 10 + 0 x 1
480.52 = (4 x 102) + (8 x 101) + (0 x 100) + (5 x 10-1) +(2 x 10-2)

## Slide 4
Any number in any base

## Slide 5
Convert the decimal number 13 to the number of base 3： [填空1]
作答
正常使用填空题需3.0以上版本雨课堂
可为此题添加文本、图片、公式等解析，且需将内容全部放在本区域内。正常使用需3.0以上版本
symbols ={0, 1, 2}
  13 = 1 * 32 + 2 * 31 + 1 * 30
  13  121
答案解析
答案解析
填空题
2分

## Slide 6
Binary Numbers（二进制数）
For digital systems, the binary number system is used. Binary has a radix of two and uses the digits 0 and 1 to represent quantities.
The column weights of binary numbers are powers of two that increase from right to left beginning with 20 =1:
…25 24 23 22 21 20.
For fractional binary numbers, the column weights are negative powers of two that decrease from left to right:
22 21 20. 2-1 2-2 2-3 2-4 …

## Slide 7
Binary Numbers
A binary counting sequence for numbers from zero to fifteen is shown.
Notice the pattern of zeros and ones in each column.
Digital counters frequently have this same pattern of digits:
0 0 0 0 0
1 0 0 0 1
2 0 0 1 0
3 0 0 1 1
4 0 1 0 0
5 0 1 0 1
6 0 1 1 0
7 0 1 1 1
8 1 0 0 0
9 1 0 0 1
10 1 0 1 0
11 1 0 1 1
12 1 1 0 0
13 1 1 0 1
14 1 1 1 0
15 1 1 1 1
Decimal Number
Binary Number

## Slide 8
Binary Conversions（二进制-十进制转换）
The decimal equivalent of a binary number can be determined by adding the column values of all of the bits that are 1 and discarding all of the bits that are 0.
Convert the binary number 100101.01 to decimal.
Example
Solution
Start by writing the column weights; then add the weights that correspond to each 1 in the number.
25 24 23 22 21 20. 2-1 2-2
32 16 8 4 2 1 . ½ ¼
1 0 0 1 0 1. 0 1
32 +4 +1 +¼ =
37¼

## Slide 10
Binary Conversions（十进制-二进制转换）
You can convert a decimal whole number to binary by reversing the procedure.
Write the decimal weight of each column and place 1’s in the columns that sum to the decimal number.(权和法)
Convert the decimal number 49 to binary.
Example
Solution
The column weights double in each position to the right. Write down column weights until the last number is larger than the one you want to convert.
26 25 24 23 22 21 20.
64 32 16 8 4 2 1.
0 1 1 0 0 0 1.

## Slide 11
1
0
0
1
1
0
You can convert decimal to any other base by repeatedly dividing by the base（反复除以基数2）.
For binary, repeatedly divide by 2（除2法）
Convert the decimal number 49 to binary by repeatedly dividing by 2.
Example
Solution
You can do this by “reverse division” and the answer will read from left to right. Put quotients to the left and remainders on top.
49 2
Decimal number
base
24
remainder
Quotient
12
6
3
1
0
Continue until the last quotient is 0
Answer:
Binary Conversions

## Slide 12
（LSB）
12110=11110012
（MSB）
Example： Convert the decimal number 121 to binary by repeatedly dividing by 2.

## Slide 13
You can convert a decimal fraction（小数） to binary by repeatedly multiplying the fractional results of successive multiplications by 2（反复乘以2）. The carries form the binary number.
Convert the decimal fraction 0.188 to binary by repeatedly multiplying the fractional results by 2.
Example
Solution
0.188 x 2 = 0.376 carry = 0
0.376 x 2 = 0.752 carry = 0
0.752 x 2 = 1.504 carry = 1
0.504 x 2 = 1.008 carry = 1
0.008 x 2 = 0.016 carry = 0
Answer = 0.00110 (for five significant digits)
MSB
Binary Conversions

## Slide 14
Convert the decimal number 39.375 to binary： [填空1]
作答
正常使用填空题需3.0以上版本雨课堂
可为此题添加文本、图片、公式等解析，且需将内容全部放在本区域内。正常使用需3.0以上版本
解：
整数部分： 3910 = 1001112
小数部分： 0.37510 = 0.0112
39.37510 = 100111.0112
答案解析
答案解析
填空题
2分

## Slide 15
Binary Addition（二进制加法）
The rules for binary addition are
0 + 0 = 0 Sum = 0, carry = 0
0 + 1 = 1 Sum = 1, carry = 0
1 + 0 = 1 Sum = 1, carry = 0
1 + 1 = 10 Sum = 0, carry = 1
When an input carry = 1 due to a previous result, the rules are
1 + 0 + 0 = 01 Sum = 1, carry = 0
1 + 0 + 1 = 10 Sum = 0, carry = 1
1 + 1 + 0 = 10 Sum = 0, carry = 1
1 + 1 + 1 = 11 Sum = 1, carry = 1

## Slide 16
Binary Addition
Add the binary numbers 00111 and 10101 and show the equivalent decimal addition.
Example
Solution
00111 7
10101 21
0
1
0
1
1
1
1
0
1
28
=

## Slide 17
Binary Subtraction（二进制减法）
The rules for binary subtraction are
0 - 0 = 0
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 with a borrow of 1
Subtract the binary number 00111 from 10101 and show the equivalent decimal subtraction.
Example
Solution
00111 7
10101 21
0
/1
1
1
1
0
14
/1
/1
=

## Slide 18
1’s Complement（反码形式）
The 1’s complement of a binary number is just the inverse of the digits. To form the 1’s complement, change all 0s to 1s and all 1s to 0s.
For example, the 1’s complement of 11001010 is
00110101
In digital circuits, the 1’s complement is formed by using inverters（反向器）:
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1

## Slide 19
2’s Complement（补码形式）
The 2’s complement of a binary number is found by adding 1 to the LSB of the 1’s complement（补码加1）.
Recall that the 1’s complement of 11001010 is
00110101 (1’s complement)
To form the 2’s complement, add 1:
+1
00110110 (2’s complement)
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1
1
0 0 1 1 0 1 1 0

## Slide 20
Signed Binary Numbers（有符号二进制数）
There are several ways to represent signed binary numbers.
In all cases, the MSB（最高位） in a signed number is the sign bit（符号位）, that tells you if the number is positive or negative.
  the sign-magnitude form(原码形式)
  the 1’s complement form(反码形式)
  the 2’s complement form(补码形式)
For example, the positive number 58 is written using 8-bits as 00111010 (true form).
Sign bit
Magnitude bits

## Slide 21
  -58：
  the sign-magnitude form：10111010
  the 1’s complement form：11000101
  the 2’s complement form：11000110
Signed Binary Numbers
Assuming that the sign bit = -128, show that 11000110 = -58 as a 2’s complement signed number:
Example
Solution
1 1 0 0 0 1 1 0
Column weights: -128 64 32 16 8 4 2 1.
-128 +64 +4 +2 = -58
Sign bit
Magnitude bits
An easy way to read a signed number that uses this notation is to assign the sign bit a column weight of -128 (for an 8-bit number). Then add the column weights for the 1’s.
58 ：00111010

## Slide 22
  Express the decimal number +1011 and -10110 as an 8-bit number in the sign-magnitude, 1’s complement, and 2’s complement forms.
[+1011]原 = [填空1]
[+1011]反 = [填空2]
[+1011]补 = [填空3]
[-10110]原 = [填空4]
[-10110]反 = [填空5]
[-10110]补 = [填空6]
作答
正常使用填空题需3.0以上版本雨课堂
填空题
6分

## Slide 23
Arithmetic Operations with Signed Numbers（有符号数计算）
Using the signed number notation with negative numbers in 2’s complement form simplifies addition and subtraction of signed numbers(用补码可以简化加减运算).
Rules for addition: Add the two signed numbers. Discard any final carries（丢弃符号位进位）. The result is in signed form.
Examples:
00011110 = +30
00001111 = +15
00101101
= +45
00001110 = +14
11101111 = -17
11111101
= -3
11111111 = -1
11111000 = -8
11110111
= -9
1
Discard carry

## Slide 24
10000001 = -127
10000001 = -127
01000000 = +64
01000001 = +65
Arithmetic Operations with Signed Numbers
10000001
= -127
100000010
= +2
Note that if the number of bits required for the answer is exceeded, overflow（溢出）will occur.
This occurs only if both numbers have the same sign.
The overflow will be indicated by an incorrect sign bit.
Two examples are:
Wrong! The answer is incorrect and the sign bit has changed.
Discard carry

## Slide 25
Arithmetic Operations with Signed Numbers
Rules for subtraction: 2’s complement the subtrahend and add the numbers. Discard any final carries. The result is in signed form. （将减法看作加法进行计算）
00001111
= +15
1
Discard carry
2’s complement subtrahend and add:
00011110 = +30
11110001 = -15
Repeat the examples done previously, but subtract:
00011110
00001111
-
00001110
11101111
11111111
11111000
-
-
00011111
= +31
00001110 = +14
00010001 = +17
00000111
= +7
1
Discard carry
11111111 = -1
00001000 = +8
(+30)
–(+15)
(+14)
–(-17)
(-1)
–(-8)

## Slide 26
Hexadecimal Numbers（十六进制数）
Hexadecimal uses sixteen characters to represent numbers: the numbers 0 through 9 and the alphabetic characters A through F.
Large binary number can easily be converted to hexadecimal by grouping bits 4 at a time and writing the equivalent hexadecimal character.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary
Express 1001 0110 0000 11102 in hexadecimal:
Example
Solution
Group the binary number by 4-bits starting from the right. Thus, 960E

## Slide 27
Hexadecimal Numbers
Hexadecimal is a weighted number system. The column weights are powers of 16, which increase from right to left.
.
1 A 2 F16
670310
Column weights
163 162 161 160
4096 256 16 1
.
{
Express 1A2F16 in decimal.
Example
Solution
Start by writing the column weights:
4096 256 16 1
1(4096) + 10(256) +2(16) +15(1) =
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary

## Slide 28
Octal Numbers（八进制数）
Octal uses eight characters the numbers 0 through 7 to represent numbers. There is no 8 or 9 character in octal.
Binary number can easily be converted to octal by grouping bits 3 at a time and writing the equivalent octal character for each group.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 10 1112 13 14 15 16 17
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Octal
Binary
Express 1 001 011 000 001 1102 in octal:
Example
Solution
Group the binary number by 3-bits starting from the right. Thus, 1130168

## Slide 29
Octal Numbers
Octal is also a weighted number system. The column weights are powers of 8, which increase from right to left.
3 7 0 28
198610
.
Column weights
83 82 81 80
512 64 8 1
.
{
Express 37028 in decimal.
Example
Solution
Start by writing the column weights:
512 64 8 1
3(512) + 7(64) +0(8) +2(1) =
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 10 1112 13 14 15 16 17
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Octal
Binary

## Slide 30
16位二进制数的最大值是什么？分别用八进制 [填空1] 、十六进制 [填空2] 、十进制 [填空3] 表示。
作答
正常使用填空题需3.0以上版本雨课堂
填空题
3分

## Slide 31
BCD（二-十进制码）
Binary coded decimal (BCD) is a weighted code （权重码）that is commonly used in digital systems when it is necessary to show decimal numbers such as in clock displays.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Binary
BCD
0001 0001 0001 0001 0001 0001
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 0000 0001 0010 0011 0100 0101
The table illustrates the difference between straight binary and BCD. BCD represents each decimal digit with a 4-bit code（每个十进制数字都用4位二进制表示）.

## Slide 32
BCD
You can think of BCD in terms of column weights in groups of four bits.
For an 8-bit BCD number, the column weights are: 80 40 20 10 8 4 2 1.
Question:
What are the column weights for the BCD number 1000 0011 0101 1001?
Answer:
8000 4000 2000 1000 800 400 200 100 80 40 20 10 8 4 2 1
Note that you could add the column weights where there is a 1 to obtain the decimal number. For this case:
8000 + 200 +100 + 40 + 10 + 8 +1 = 835910

## Slide 33
Convert the decimal number 275.5 to 8421BCD [填空1] and binary [填空2] 。
作答
正常使用填空题需3.0以上版本雨课堂
填空题
2分

## Slide 34
Gray code（格雷码）
Gray code is an unweighted code （无权码）that has a single bit change between one code word and the next (相邻数之间的码只有一位变化)in a sequence.
Gray code is used to avoid problems in systems where an error can occur if more than one bit changes at a time.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Binary
Gray code
0000 0001 0011 0010 0110 0111 0101 0100 1100 1101 1111 1110 1010 1011 1001 1000

## Slide 35
ASCII
ASCII is a code for alphanumeric characters and control characters（字母数字字符和控制字符的编码）.
In its original form, ASCII encoded 128 characters and symbols using 7-bits. The first 32 characters are control characters, that are based on obsolete teletype requirements, so these characters are generally assigned to other functions in modern usage.
In 1981, IBM introduced extended ASCII, which is an 8-bit code and increased the character set to 256. Other extended sets (such as Unicode) have been introduced to handle characters in languages other than English.

## Slide 36
000 001 010 011 100 101 110 111
NUL DEL SP 0 @ P 、 p
SOH DC1 ! 1 A Q a q
STX DC2 " 2 B R b r
ETX DC3 # 3 C S c s
EOT DC4 $ 4 D T d t
ENQ NAK % 5 E U e u
ACK SYN & 6 F V f v
BEL ETB , 7 G W g w
BS CAN ( 8 H X h x
HT EM ) 9 I Y i y
LF SUB * ： J Z j z
VT ESC + ； K ［ k {
FF FS ， < L ＼ l |
CR GS - = M ］ m }
SO RS . > N ∧ n ～
SI US / ? O － o DEL
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
高3位代码(a7a6a5)
低4位代码 (a4a3a2a1)
ASCII

## Slide 37
Parity Method（奇偶校验）
The parity method is a method of error detection for simple transmission errors involving one bit (or an odd number of bits).
A parity bit（校验位） is an “extra” bit attached to a group of bits to force the number of 1’s to be either even (even parity偶校验) or odd (odd parity奇校验).（增加校验位保证1的个数都为奇数或者都为偶数）
The ASCII character for “a” is 1100001 and for “A” is 1000001. What is the correct bit to append to make both of these have odd parity?
Example
Solution
The ASCII “a” has an odd number of bits that are equal to 1; therefore the parity bit is 0. The ASCII “A” has an even number of bits that are equal to 1; therefore the parity bit is 1.

## Slide 38
The cyclic redundancy check (CRC) is an error detection method that can detect multiple errors in larger blocks of data.
At the sending end, a checksum（校验和） is appended to a block of data.
At the receiving end, the checksum is generated and compared to the sent checksum. （接收端将计算得到的校验和和传输来的校验和进行比较来验证数据的正确性）
If the check sums are the same, no error is detected.
Cyclic Redundancy Check（循环冗余校验）

## Slide 39
Selected Key Terms
Byte
Hexadecimal
Octal
BCD
A group of eight bits
A number system with a base of 16.
A number system with a base of 8.
Binary coded decimal; a digital code in which each of the decimal digits, 0 through 9, is represented by a group of four bits.

## Slide 40
Selected Key Terms
ASCII
Parity
Cyclic redundancy check (CRC)
American Standard Code for Information Interchange; the most widely used alphanumeric code.
In relation to binary codes, the condition of evenness or oddness in the number of 1s in a code group.
A type of error detection code.

## Slide 41
1. For the binary number 1000, the weight of the column with the 1 is
a. 4
b. 6
c. 8
d. 10
Quiz

## Slide 42
2. The 2’s complement of 1000 is
a. 0111
b. 1000
c. 1001
d. 1010
Quiz

## Slide 43
3. The fractional binary number 0.11 has a decimal value of
a. ¼
b. ½
c. ¾
d. none of the above
Quiz

## Slide 44
4. The hexadecimal number 2C has a decimal equivalent value of
a. 14
b. 44
c. 64
d. none of the above
Quiz

## Slide 45
5. Assume that a floating point number is represented in binary. If the sign bit is 1, the
a. number is negative
b. number is positive
c. exponent is negative
d. exponent is positive
Quiz

## Slide 46
6. When two positive signed numbers are added, the result may be larger that the size of the original numbers, creating overflow. This condition is indicated by
a. a change in the sign bit
b. a carry out of the sign position
c. a zero result
d. smoke
Quiz

## Slide 47
7. The number 1010 in BCD is
a. equal to decimal eight
b. equal to decimal ten
c. equal to decimal twelve
d. invalid
Quiz

## Slide 48
8. An example of an unweighted code is
a. binary
b. decimal
c. BCD
d. Gray code
Quiz

## Slide 49
9. An example of an alphanumeric code is
a. hexadecimal
b. ASCII
c. BCD
d. CRC
Quiz

## Slide 50
10. An example of an error detection method for transmitted data is the
a. parity check
b. CRC
c. both of the above
d. none of the above
Quiz

## Slide 51
Answers:
1. c
2. b
3. c
4. b
5. a
6. a
7. d
8. d
9. b
10. c
Quiz

## Slide 52
作业
P53 Self-Test 1-18
Problem：
  28
  34
  50 g h i
  59
  60